## Slide 1: M.C. Studies of CDC Axial/Stereo Layer Configuration
David Lawrence, JLab
Sept. 19, 2008

## Slide 2: How c2 is defined
The c2 is formed using the residuals between the fit and thrown parameters:
If the components are independent and drawn from a Gaussian parent distribution, this would follow a “chi-squared” distribution with a well-known probability distribution

## Slide 3: Map of c2/dof as a function of 2 of the 5 fit parameters
Event A
Event B

## Slide 4: Event 1914 has a large c2/dof
A bird’s eye view of the event looks like everything is OK
Blue (thick) is the thrown track
Orange (thin) is the fit track

## Slide 5: Event 1914 has a large c2/dof
X-Y view of Event 1914
Thrown track
Fit track

## Slide 6: Event 1179 has a large c2/dof
X-Y view of Event 1179
Thrown track
Fit track

## Slide 7: Other events with poor c2/dof with pt as dominant term
Event 1277
Event 2342

## Slide 8: Two options for CDC stereo configuration
2 stereo superlayers
3 stereo superlayers
stereo8
stereo9

## Slide 9: Alignment of CDC straws
df relative to the f of the wire in layer 23 as a function of f.
Pattern comes from neighboring layers having only slightly more (or less) straws than layer 23.
f values with high density of points indicate areas where there is a high degree of alignment.

## Slide 10: Alignment of CDC straws w/ phase shifts
To disrupt the alignment of the wires, phase shifts in f were introduced for each layer.
Every 4th layer was rotated by:
  0
  +Dfi/2
  -Dfi/3
  +Dfi/5
where Dfi is the angle between adjacent wires in the layer

## Slide 11: Reciprocal of phase difference density
In this plot, larger values indicate greater alignment of the straws in the outer layers (15-25).
The stereo9 configuration is slightly better than stereo8, but both are improved significantly by adding relative phase shifts between layers.

## Slide 12: 5 CDC configurations studied (yes, only 4 are shown)
24 layers
27 layers

## Slide 13: What was simulated
1 million single p+ events for each configuration. MS, E-loss on, but no position smearing
Finder and fitter used in conjunction (previously, all fit results came from using the thrown values for the candidates)
Efficiency determined by cut on c2/dof derived from parameters (not hit residuals)

## Slide 14: “Tracking Efficiency” compared to c2 cumulative distribution function

## Slide 15: Pulls with double Gaussian fits
Red = Tracking Results
Thick black = double gaussian
Thin black = gaussian (sampled)
df
dpt/pt
dq
c2

## Slide 16: Efficiency as a function of phase space
0.2 GeV/c ≤ p ≤ 2.0 GeV/c
15o ≤ q ≤ 140o

## Slide 17: Toy model c2 shares features with MC Simulation study
MC Simulation with reconstruction
Toy model plot (left) includes all L-R solutions (including 15 “wrong” ones)
MC Simulation includes 1 guess for L-R solution

## Slide 18: Probability Distributions for two ways of fitting pull distributions
Gaussians fit only to core of pull distributions
Gaussians fit to full pull distributions

## Slide 19: Tracking Efficiency for Several CDC Configurations
Phasespace: range

## Slide 20: dE in single tube reported by hdgeant
Nominal Geometry
Close Packed
Green regions are estimates of hits discarded by dE threshold. Estimate is made by straight line from 0,0 to 1keV point. This likely overestimates the below-threshold contribution.
NOTE: Max energy deposition at 90o : (1.6 cm)(2.6 keV/cm) = 4.16 keV
Phasespace: 1 GeV/c ; 90o

## Slide 21: CDC hits per track
Nominal Geometry
Close Packed
The number of missing hits was fit to a Poisson and the mean taken as the average number of missed hits.
The Nominal Geometry is consistent with the single hit efficiency derived from the dE plots.
The Close Packed geometry is consistent with ~9% inefficiency on average due to gaps in the “close-packed” axial layers.
Phasespace: range

## Slide 22: Distance of Closest Approach (DOCA) (calculated from tdrift-tof)
Nominal Geometry
Close Packed
Phasespace: 1 GeV/c ; 90o
DOCA distributions seem consistent with the 88.2% single hit efficiency and cut on dE which corresponds to the outer part of the tube.

## Slide 23: Expected energy loss in CDC gas
Total for CDC gas dE/dx = 2.597 keV/cm
 | dE/dx (MeV/g cm2) | r (g/l) | dE/dx (keV/cm)
Ar (85%) | 1.519 | 1.622 | 2.464
CO2(15%) | 1.819 | 1.842 | 3.351
a
x
= 1.26cm
3.27 keV
Note: for a 1 keV energy loss, expect x=7.8mm or about 2.45% inefficiency

## Slide 24: Tracking Efficiency with and without dE threshold
Phasespace: range

## Slide 25: Close packing vs. extra layers
The low-threshold baseline design (shifted) has approximately the same number of hits per track as the close packed design with a high threshold. This gives a suggestion as to how much close packing buys vs. extra layers.
2 stereo superlayers

## Slide 26: Conclusions
3 stereo superlayers improves tracking efficiency
Additional layers improves tracking efficiency (we seem to be in a region of high sensitivity)
Single hit efficiency due to 1keV threshold is ~88%. The energy distribution from hdgeant needs to be verified and then the threshold examined more closely
c2 distribution is not yet fully understood, but tests are underway to see if it is linked to the Left-Right ambiguity issue

## Slide 27: Backup Slides

## Slide 28: Gaussian fits to full pull distributions (not just Gaussian cores)

## Slide 29: Expected Probability Density as a Function of the Integral Fraction

## Slide 30: Efficiency as a function of transverse momentum and polar angle
stereo8
stereo9
Differences not really noticeable here!
Total momentum range: 150MeV/c - 2GeV/c
Total angular range: 15o – 140o

## Slide 31: Pulls of momentum parameters for CDC option-1 and option-2

## Slide 32: Efficiency vs. accuracy of fit parameters

## Slide 33: Pulls from fits with perfect conditions for stereo8
off

## Slide 34: Why “perfect” isn’t perfect
hdgeant estimates the point of closest approach (POCA) to be the midpoint of the entrance and exit points of the tube. This is true to about 10 mm (systematic)
Tracking reconstruction approximates trajectory as parabola near wire and calculates POCA from that

## Slide 35: Efficiency for “perfect” conditions