## Slide 1: Level-1 Trigger Commissioning Status
A.Somov Jefferson Lab
Collaboration Meeting, May 10, 2010

## Slide 2: Trigger Commissioning and Monitoring Tools
GlueX Level-1 trigger group responsibilities are to commission the trigger electronics
and provide tools for monitoring the trigger performance.
Main tools:
• Test Vector
• Trigger monitors
Test Vector:
• Check performance of the electronic boards (synchronization, code loaded to FPGAs…)
and calibration constants.
• Verify the trigger algorithm.
• Will be performed during the trigger commissioning phase and before taking the data.
Implementation:
• Write predefined signal shapes to the FADC250’s FPGA memory.
• Run the trigger hardware.
• Compare hardware output with the MC predictions.
Trigger Monitors:
• Perform online monitoring of the trigger rates, occupancies, … during data taking
• Will be implemented as scalers residing inside FPGAs.
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 2

## Slide 3: Test Vector Implementation
Load FADC amplitudes of signal pulses to FPGA’s memory.
Trigger Supervisor initiates processing of the samples through the trigger hardware.
Play Back signal will be delivered to the FADC through one of the trigger lines.
• • • 16 ch
• • • 16 ch
• • • 1 - 16 FADC
FADC
FADC
TS
SSP
SSP
GTP
CTP
SD
TI
SD
TD
Play Back
Trigger
• • • 1 - 8
Hai Dong
Ed Jastrzembski
David Abbott
Ben Rayado
Alex Somov
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 3

## Slide 4: Play Back Mode: FADC
LX25
LX25
FX20 
Altera FPGA
FIFO
FIFO
CTP
VMEbus
Self Trigger
Load Samples to Memory
Play Back
Trig from TI
(one line for play back)
Load amplitudes of signal pulses (samples) to FPGA memory.
Play Back pulse width defines how many samples to process.
Trigger from TI initiates the VME readout (trigger can also be initiated by FX20 –
self trigger mode)
play back pulse
pulse in the memory
16 x 4 ns = 64 ns (currently)
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 4
Current version of FADC250

## Slide 5: Trigger Test Stand
Pulse
Generator
TI
FADC
ROCK
Discriminator
Delay
Trig IN
Trigger
Trig IN
Trig OUT
VME
Play Back
- CODA
- Load Samples
Maximum width of a signal pulse loaded to the memory: 16 x 4 ns. The same pulse shape is
loaded to all 16 channels.
Play Back signal is send to FADC through the VME P2 bus.
Use external trigger. TI initiates trigger interrupt.
FADC is operated in the “Window Raw Data” mode (read out specified number of samples).
Other readout modes have been checked as well (Pulse Raw Data, Pulse Integral).
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 5

## Slide 6: Trigger Test Stand
FADC in the Window Raw Data mode
Play Back pulse
Readout Window
Loaded Pulse
The same pulse shape for all 16 channels.
Some work is needed to be able to load
different pulse shapes into different FADC
channels.
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 6
Load 11 amplitudes (samples) into
FADC memory.
The Play Back pulse width: ~ 70 ns.

## Slide 7: Summary / Future Plans
We have started preparing for the Level-1 Trigger commissioning.
We received a lot of support/help from the Fast Trigger Electronics and DAQ groups.
Next Steps:
Finish with implementation of the “Play Back” mode – should be able to write
different samples to the16 FADC channels.
We are on the way to the 2 crate test stand.
- The new TI prototype and the new FADC version will be ready by the fall of 2010.
- DAQ official software is under development.
Level 1 Trigger Commissioning Status, GlueX Collaboration Meeting, May 10, 2010 7