## Slide 1: The GlueX Detector
David Lawrence (JLab)
Electron beam accelerator
  continuous-wave (1497MHz, 2ns bunch structure in halls)
  Polarized electron beam
  Upgrading to 12GeV (from 6GeV)
  70 mA max @ 12Gev (200mA max @ 6GeV)
Existing experimental halls A, B, C
Future Hall-D site

## Slide 2: The GlueX Experiment
9GeV linearly polarized
hybrid meson
detectable final state
(mixed charged and neutral)
Goal: map the spectrum of exotic hybrid mesons
Method: Photo-produce hybrids off proton target and identify the quantum states using Partial Wave Analysis of decay product distributions
See Matt Shepherd’s and Jo Dudek’s talks Saturday @ 16:30 “QCD, Hadron Spectroscopy and Exotics” session

## Slide 3: Hall-D Complex at Jefferson Lab
~100 meters
electron beam
Construction has recently begun and will be completed Fall 2011. (Buildings only, detectors will follow)

## Slide 4: The Photon Beam
4
1.5T dipole magnet
12m long vacuum chamber
e-
20mm diamond radiator
photon energy (GeV)
coherent bremstrahlung spectrum
Microscope:
Movable to cover different energy ranges
100 x 5 scintillating fibers (2mm x 2mm)
800MeV covered by whole microscope
100MHz tagged g/sec on target
~8MeV energy bite/column
Fixed array hodoscope:
190 scintillators
50% coverage below 9GeV g
100% coverage above 9GeV g
Tags 3.0-11.7 GeV g
~30MeV energy bite/counter
3.5 – 17 MHz/counter
Photon Polarization:
20 mm diamond radiator
Coherent peak is linearly polarized
~40% polarization with peak @ 9GeV
Peak location tunable with diamond angle

## Slide 5: The GlueX Detector
TOF
time of flight
SC
start counter
2.2T superconducting solenoidal magnet
Fixed target (LH2)
108 tagged g/s (8.4-9.0GeV)
hermetic
2.2 Tesla
Solenoid
Calorimetry
Barrel Calorimeter (lead, fiber sandwich)
Forward Calorimeter (lead-glass blocks)
PID
Time of Flight wall (scintillators)
Start counter
Barrel Calorimeter
Charged particle tracking
Central drift chamber (straw tube)
Forward drift chamber (cathode strip)

## Slide 6: A single g p  pb1p event
Final state: p p+ p+ p- p- po

## Slide 7: Calorimetery
Calorimeters measure the energy of single, energetic particles
To do this, the energy must be converted into a measurable form
Several detectors available that convert a fraction of the energy to light
Light detected by photo-sensitive devices
For GlueX, calorimeters designed to measure gs (not hadrons)
Material needs to be:
Thick
Dense
Optically Clear
Incident g will generate a “shower” through a series of E.M. interactions
e+/e- pair production
g production via bremstrahlung

## Slide 8: BCAL: Barrel Calorimeter
Barrel Calorimeter:
191 layer Pb-scintillating fiber sandwich (15.5Xo)
12.5% sampling fraction
1152 + 192 = 1344 readout sections/end
sE/E= (5.54/√E 1.6) %
sz = 5mm/√E
st = 74ps/√E 33ps
angular coverage 11o < q < 120o
illustration does not accurately represent the number of photo-detection devices
Light Guides
Photo-detection devices
BCAL module being constructed
BCAL has 2-ended readout allowing one to reconstruct in 3-D
390 cm

## Slide 9: FCAL: Forward Calorimeter
Forward Calorimeter:
2800 F8-00 and F108 (center) Pb-glass blocks
4cm x 4cm x 45cm
sE/E= (5.7/√E 2.0) %
sxy = 6.4mm/√E
angular coverage 2o < q < 11o
Prototype FCAL Array
An FCAL module
Lead-glass produces Cerenkov light (not scintillation light!)

## Slide 10: Charged Particle Tracking
Time: 234 ns
DIST: 3.337 mm
Time-of-flight: 27 ns
Wire ID: 1329
DOCA: 3.425 mm
residual: 88 m
Drift chambers are used to measure single, energetic charged particles
To do this, the particle is passed through a region with a strong magnetic field
The field curves the path of the particle in a way that depends on its momentum
Drift chambers measure position of particle at several places (15-30) along its trajectory
Easily ionizable gas (Ar CO2) in chambers allows charged particle to leave trail of electron/ion pairs
Electrons drift to the “sense” wire due to high voltage induced electric field
Drift time related to drift distance

## Slide 11: CDC: Central Drift Chamber
Central Drift Chamber:
3522 straw tubes (1.6cm diameter)
12 axial layers, 16 stereo layers (6o)
dE/dx for p < 450 MeV/c
sr = 150mm
angular coverage 6o<q<155o
sp/p : 1.5 - 3.0%
CAD drawing of CDC
A straw tube being cut
CDC prototype II
Track is fit to tangent points of circles representing drift distance

## Slide 12: FDC: Forward Drift Chamber
Forward Drift Chamber:
4 packages, 6 planes/package, 96 wires/plane (2304 sense wires)
cathode strip readout (48 planes x 216 strips/plane = 10,368 strips)
sr = ~200mm perpendicular to wire (drift time)
ss = ~200mm along wire (cathode strips)
angular coverage 1o<q<30o
FDC Cathode Plane
Illustration of FDC wire plane and cathode planes
Electric field around 1 FDC wire
FDC planes rotated 60o wrt neighbors
FDC Frames
FDC Active Area

## Slide 13: Particle ID
diff (ps)
pp separation <450MeV/c
pK separation <275MeV/c
Barrel Calorimeter
Forward TOF
diff (ns)
~200 ps
~80 ps
CDC dE/dx
40 scintillators
300 ps (w/tracking)
Used for start-up
Start Counter
Particle ID is done primarily through time of flight with some help from dE/dx in chambers. Space is left in design for a future PID detector.
Beam Test Data
Expected Separation

## Slide 14: Electronics and Data Rates
Electronics
All digitization electronics are fully pipelined (VME64x-VXS)
  F1TDC (60 ps, 32 ch. or 115 ps 48 ch.)
  125 MHz fADC (12 bit, 72 ch.)
  250 MHz fADC (12 bit, 16 ch.)
Trigger latency ~3 ms
3GB/s readout from front end
300MB/s to mass storage
3PB/yr to tape
Offline software
C++ object oriented framework (JANA)
Multi-threaded event processing
Highly modular through use of templates
Crate Trigger Processor
F1TDC
Level 1 trigger test stand
Signal distribution board

## Slide 15: Trigger System
slide stolen from C. Cuevas’ talk at May 2010 GlueX Collab. Meeting

## Slide 16: Summary
The GlueX detector is a large acceptance, hermetic detector with a solenoidal geometry
  Capable of detecting multi-charged, multi-neutral final states with high resolution
  Fully pipelined electronics allow 3 ms trigger latency and a 3GB/s data rate off the front end (300MB/s to disk)
See Matt Shepherd’s and Jo Dudek’s talks Saturday @ 16:30 “QCD, Hadron Spectroscopy and Exotics” session

## Slide 17: Backups

## Slide 18: The JLab 12GeV Upgrade
6 GeV CEBAF
11 GeV CEBAF
CHL-2
12 GeV CEBAF
Upgrade magnets and power supplies
Two 0.6 GV linacs
Two 1.1GV linacs
Enhanced capabilities
in existing Halls
Notes: help me

## Slide 19
Page 19
Capability | Quantity | Range
Charged particles | Coverage | 1o < q < 160o
 | Momentum Resolution (5o-140o) | sp/p = 1 − 3%
 | Position resolution | s ~ 150-200 mm
 | dE/dx measurements | 20 < q < 160o
 | Time-of-flight measurements | sToF ~ 60 ps; sBCal ~ 200ps
 | Barrel time resolution | st g < (74 /√E 33) ps
Photon detection | Energy measurements | 2o < q < 120o
 | LGD energy resolution (E > 60 MeV) | sE/E = (5.7/√E 2.0)%
 | Barrel energy resolution (E > 60 MeV) | sE/E =(5.54/√E 1.6)%
 | LGD position resolution | sx,y, ~ 0. 64 cm/√E
 | Barrel position resolution | sz ~ 0.5cm /√E
DAQ/trigger | Level 1 | < 200 kHz
 | Level 3 event rate to tape | ~ 15 kHz
 | Data rate | 300 MB/s
Electronics | Fully pipelined | 250 / 125 MHz fADCs, TDCs
Photon Flux | Initial: 107 g/s | Final: 108 g/s
Hall D: Detector Design Parameters

## Slide 20: Electronics and Data Rates
125MHz fADC layout
Electronics
All digitization electronics are fully pipelined (VME64x-VXS)
  F1TDC (60 ps, 32 ch. or 115 ps 48 ch.)
  125 MHz fADC (12 bit, 72 ch.)
  250 MHz fADC (12 bit, 12 ch.)
Trigger latency ~3 ms
3GB/s readout from front end
300MB/s to mass storage
3PB/yr to tape
Offline software
C++ object oriented framework (JANA)
Multi-threaded event processing
Highly modular through use of templates