## Slide 1
GlueX Collaboration Meeting
12GeV Trigger Electronics
2-4 February 2011
R. Chris Cuevas
  Hardware Design Status Updates
    The regular list of acronyms
      SD; TI-D; SSP; CTP; GTP; TS
    Trigger System – Fiber Optics
    Preparation for full crate testing
  1st Article VXS Crate Testing
  Summary

## Slide 2
Flash ADC 250Msps ( FADC250 )
  This is where the trigger ‘data’ begins
  ** Version 2 design complete – See Fernando’s update **
  Many tests have been completed!
  Significant layout revision with consolidation of firmware and FPGA
Crate Trigger Processor ( CTP )
  ** 2 units tested in 2009 ** 2 more sent for assembly Sept-2010
  2 new CTPs assembled and received. New modules have different FPGA and support higher Gigabit speed (5Gbps)
  Initial CTP used for verification of new WIENER VXS backplane
  New boards will be thoroughly tested and used in full crate test plan
  Collects trigger data (SUM) from 16 FADC250 modules within one crate
  Transports trigger data over fiber to Global Trigger crate
    10Gbps capability ( 8Gbps successfully tested )
2
Trigger Hardware Status

## Slide 3
Signal Distribution ( SD )
  2 prototypes tested in 2009 ** Rev-1 ready to manufacturer Oct-2010 **
  Precision low jitter fan-out of ADC clock, trigger and synch signals over VXS backplane to FADC250 modules
  Minor revisions to include clock jitter attenuation PLL
  2 Rev-1 boards have been assembled and received
  A few power supply issues have been resolved, and updates to firmware have been completed to support jitter attenuation PLLs
  I^2C communication with latest TI-D has been tested
  We have components for at least six more units
  Two boards will be used for full crate testing before ordering pre-production quantities. (June 2011)
3
Trigger Hardware Status

## Slide 4
Trigger Interface – Trigger Distribution ( TI - TD )
  FY10 Goals achieved.
  FY11 test goals are ahead of schedule and firmware has been completed.
  Design changes have been recorded and peripheral modules for TI-D have been completed. (i.e. Fan-out board for CAEN V1290 TDC)
  CODA library has been updated for latest TI-D revision.
  After full crate testing, pre-production quantities will be ordered.
  Direct link to Trigger Supervisor crate
  Distributes precision clock, triggers, and sync to crate SD
  Manages crate triggers and ReadOut Controller events
4
Trigger Hardware Status

## Slide 5
SubSystem Processor ( SSP )
  Prototype received and is undergoing detailed functional testing!!
  FY10 goals achieved and FY11 test activities will continue
  Will use SSP during full crate testing in the spring
  Collects trigger data from up to 8 front end crates. (2048 channels!)
  Trigger data received on front panel with fiber transceivers
  10Gbps input capability ( 4 lanes @3.125Gbps*(8/10b) )
  10Gpbs output stream to GTP
Global Trigger Processor ( GTP ) (FY10-11)
  Schematic work is back on schedule (Scott Kaneta )
  FY11 goal is to build initial prototype and test with SSP and TI-D
  Revisions to initial specification has been updated and finalized
  Interface requirements to SSP and TS have been finalized
  Large scale FPGA has been selected and Xilinx Aurora protocol has been tested with Altera FPGA
5
Trigger Hardware Status

## Slide 6
6
Trigger Hardware Status
Trigger Supervisor ( TS ) (FY11-12)
  New board format – VXS Payload module
  Distributes precision clock, triggers, and sync to crate TI-TD
  Manages crate triggers and ReadOut Controller events
  Direct cable link to Global Trigger Processor (32 trigger bits)
  Specification has been updated to match GTP output
  Schematic and board layout activities can begin after full DAQ crate testing is complete and pre-production orders for TI-D and other boards have been completed.

## Slide 7
Discriminator Status
(Not truly trigger system hardware, but very nice new development)
16 Pre-Production modules have been assembled and received
Significantly cheaper than V895:
  -cost < $2,000
Provides several features not found on V895:
  32bit scalers on all channels at both thresholds
  Calibrated pulse widths: from 8 to 40ns
  Trimmed input offset (<2mV error)
  Second 34pin output connector is fully programmable.
  Able to perform logic based on all channels at both thresholds
Final revision has VME64x J1-J2 connector
Full test stand developed by Pedro Toledo(USM – Chile) will be re-used
Hall Groups will test with detectors
Ben Raydo
7
16 modules in crate
Pre-Production version
Note: VME64x connectors

## Slide 8
CTP Prototype:
Crate Trigger Processor
4 Fully assembled units are in the lab!!
2 newest units include VirtexV FX70T that supports higher serial speeds. (5Gbps) Matches FX70T on FADC250
Initial CTP unit used to verify new WIENER VXS backplane map
Crate Trigger Processor computes a crate-level energy sum (or hit pattern)
Computed crate-level value sent via 10Gbps fiber optics to Global Trigger Crate (32bits every 4ns)
Crate Sum/Hits
10Gbps Fiber to SSP in global trigger crate
Board Energy/Hits
Up to 10Gbps to CTP
Fiber Optics Transceiver
VXS Connectors
Collect serial data from 16 FADC-250
8

## Slide 9
N. Nganga
10-Oct-2010
14
9
Crate Level – Signal Distribution (SD) -Rev 1
VITA 41
Switch
Slot
Connectors
Two boards fully assembled and almost completely tested

## Slide 10
Crate Level – Signal Distribution (SD) -Rev 1
New power regulation scheme tested
New (final) front panel complete
Token In/Out tested
Latest I^2C firmware has been tested with TI-D.
Supports the control of the on board PLLs from
the FPGA via SPI. Users can select Jitter Attenuation mode (PLL) or non-PLL mode.
All common signals from TI ( i.e. Busy, Sync, Trig1, Trig2 have been tested.
Final results from PLL jitter attenuation tests will be completed before 15-Feb-2011
N. Nganga
M. Taylor
C. Cuevas
10

## Slide 11
TID Components
Eight
Optical Transceivers
HFBR-7924
‘Legacy’
Trigger
Supervisor
Interface
External I/O
(trg, clk…)
VMEPROM
(FPGA firmware)
Emergency/remote
re-programming
VXS P0
TD mode: from SD
TI/TS mode: to SD
VME 64x
One dedicated link for redundant data collection
Trg/Clk/Syc
outputs
On row_C
Xilinx
VirtexV
LX30T-FG665
Trigger Interface - Distribution
11
W. Gu
DAQ Group

## Slide 12
What is tested:
The power distribution for the board is tested and working.
All the discrete components (drivers, buffers, receivers etc)
are tested, and working
The on-board clock distribution network is working.
The on-board trigger distribution network is working.
Serialized trigger data re-sampling (ADN2805).
FPGA firmware:
    VME to I2C engine;
    VME data readout;
    VME remote firmware loading;
    Customized the firmware for TI, TD, mini-TS mode
    Initial Jitter analysis results for 250MHz clock are low ~2ps
Trigger Interface - Distribution
12
W. Gu
DAQ Group
2/2/2011

## Slide 13
The scope used: Tek7254, probe: TDS3500 differential probe
Scope setting: 40GS/sec  25 Ps/Pt, 2.5 GHz limited
Measuring software: TDSJIT3 ADVANCED, 400K samples (auto set)
or DPOJET ESSENTIAL, 50M samples.
Measured on TID#2, TID#1 may be used as clock source
Clock Osc
Mux
Buffer
HFBR
HFBR #1
HFBR #5
Clock Osc
Mux
Buffer
P0
ClkC
ClkA
DPO7254, TDSJIT3, DPOJET
TID#1
TID#2
Measurement diagram
TI-TD Testing
W. Gu
DAQ Group
13

## Slide 14
Assuming that the oscillator has negligible jitters, the TID to P0 distribution has a jitter of less than 2ps, and the two HFBR_7924/34 distribution has a jitter of less than 2ps too ( sqrt(2.65*2.65-1.88*1.88)=1.87ps ).
TID#2 on-board oscillator as clock source, the ClkC jitter measured: 1.88ps
TID#2, HFBR#5 as clock source, the ClkC jitter measured: 2.65ps
TI-TD Testing
W. Gu
DAQ Group
14

## Slide 15: SSP Prototype
VME64x
(2eSST support)
VXS-P0
(up to 16Gbps to each GTP)
Optional DDR2 Memory Module (up to 4GByte)
8x Fiber Ports ( 10Gbps each to CTP )
2x NIM
(bidirectional)
4x ECL/PECL/LVDS In 4x LVDS Out
Ben Raydo
9-Sept-2010
15

## Slide 16
SSP Working with CTP
SSP
CTP
10Gbps ‘Ribbon’ Fiber
4Tx 4Rx
Ben Raydo
9-Sept-2010
16

## Slide 17
SSP
“Optic Probe”
8GHz Scope
Fiber optics
COAX
Eye analysis
400ps Bit Width
Very wide receiver eye (0.8UI) at 1E-12 BER.
UI = Unit Interval = 1/Bit Rate
Gigabit transceivers & optics are performing much better than device specifications – further testing will reveal accurate bit-error rate estimates.
0 Crossing Jitter
SSP 2.5Gbps Fiber Eye (1 of 32 shown)
Single Ended Capture (amplitude is really double what’s seen).
Reflections mainly due to test fixture.
Tektronix DSA70000
Ben Raydo
9-Sept-2010
17
Time-Interval-Error
FPGA  F/O Transceiver

## Slide 18
SSP Summary
BGA assembly issues have been resolved.
SSP will be used for two DAQ crate testing in spring.
Link quality tests remain between fibers and FPGAs, as well as FPGA and FPGA, but is looking very good so far.
DDR2 Memory testing needs to be completed
Testing with GTP will have to wait for GTP prototype. (June ‘11)
SSP Project ahead of schedule!
Ben Raydo
1-Feb-2011
18

## Slide 19
Global Trigger Processor: (GTP)
Trigger Decisions
to Trigger Distribution Crate
{Trigger Supervisor}
Global Trigger Processor (GTP) receives all subsystem Level 1 data streams from SSP
Trigger decisions made in GTP and distributed to all crates via the Trigger Distribution (TD) modules in the Trigger Supervisor Crate
Schematics and component selection activities are progressing well
Preliminary component placement and layout strategies have been completed
Xilinx’s ‘Aurora’ Gigabit protocol has been ported to Altera device successfully
19

## Slide 20
TS
GTP
Switch A
SD
Switch B
SSP 1
Payload 1
CTP
1
TI
Payload 18
CTP
8
.
.
.
SSP 16
Payload 16
CTP 121
CTP 128
.
.
.
.
.
.
Global Trigger Crate
Fiber
Trigger Distribution Crate
32
4
4
/
4
/
4
/
4 x 8 LVPECL
‘Densishield’
Scott Kaneta
Jan-2011
Global Trigger - Block Diagram:
20

## Slide 21
Configuration Controller CPLD
Altera Stratix IV GX
180
Front Panel
RJ45
PHY
Trigger Out
Multi-Image Configuration Flash
DDR2
Code Flash
Link Up 0
2
/
SSP Data 0
Link Up 15
2
/
SSP Data 15
.
.
.
VXS Backplane
Clock, Sync
Trig1, Trig2
Nios II
Processor(s)
Ethernet
Ethernet
RGMII
4x Densishield
4
/
/
32
JTAG
High Speed
General Purpose
Configuration
Legend
/
4
Fiber Transceiver
LVDS
Global Trigger Processor: (GTP)
36 Transceivers at 8.5 Gbps
Scott Kaneta
Jan-2011
21

## Slide 22
/
32
Global Trigger Processor: (GTP)
Scott Kaneta
Jan-2011
Ethernet
Altera FPGA
MTP Fiber TxRx
JTAG
+5VDC
VXS
Switch
Slot
LVPECL 4 x 8 pair to TS (P2)
22

## Slide 23
Other Trigger System Essentials
VXS and VME64x powered card enclosures
  Crate specification complete
  Multi-year contract awarded to W-IE-NE-R, Plein & Baus, Ltd.
  First article crates (VXS) received 24-Jan-2011
  Acceptance tests nearly complete
  (6) –> VME64x & (8) –> VXS crates will be delivered before May-2011
    Will need storage location!!
23
+5VDC; Ripple Measurement
<10mVp-p; 50A load
Hartman VXS 21 Slot Backplane
CTP @2.5Gbps to each payload port
Correctly mapped

## Slide 24
Other Trigger System Essentials Trigger System Fiber Optics FY11 Work Plan
23
System diagrams have been updated for Hall D installation
Preparing for procurement now! (Material and installation labor)
Final component specifications are complete
  i.e.(Fiber patch panels, Fiber (trunk) cables, MTP patch cables, etc)
24

## Slide 25
Two DAQ Crate Testing: FY11
Several modules have been revised and will need to be thoroughly tested. (FADC250, SD, TI-D)
The initial SSP will be used to sum the trigger data from 2 CTP
Multiple crate ‘system level’ testing is imperative before approving large quantity orders.
  Will verify Gigabit serial lanes from each slot
    1st Time for 16 boards!!!
  Will measure trigger latency
  Will measure trigger rates/VME data rate
  Will measure BitErrorRates
  Will test using “Playback” mode
    (No input cables necessary)
Perfect opportunity to fully test latest revision
of CODA board ‘libraries’
Plan to use latest CPU as proposed by DAQ group
Front End Crate:
25
2.5Gbps/
VXS lane

## Slide 26
Summary
FY10 board design project goals have been achieved
FY11 plan includes aggressive test plans for all modules
GTP prototype and completion of FINAL revisions for trigger modules in FY11
High level of detailed design work is exemplary and board tests meet specification
Work activity schedule shows estimate to completion plan is reasonable
  Production quantities for all halls have been considered
2 full DAQ crates with all trigger module units will be tested in spring
Time to think about 4th annual 12GeV Trigger Workshop
  Will have plenty of results from full crate testing
  Plenty of other work remains for pre-commissioning ‘tools’ and test plans
Weekly 12GeV Trigger meeting continues to produce good discussions and ideas
for implementation of system level test programs and details of hardware designs.
26

## Slide 27
All sorts of good stuff
Backup Slides

## Slide 28
GlueX Level 1 Timing
21

## Slide 29
Schedules, work plans for FY11 - FY13
FY10 design projects are at full resource pace!
  FADC250  Latest revision at end of FY10. TEST in FY11.
  F1TDC-V2 Work plan moved to FY11
  SD  Latest revisions virtually complete. Order, assemble, TEST in FY11
  SSP  Prototype received. Initial testing is proceeding nicely.
        Further testing in FY11.
  TI-TD  Prototype(s) received. Initial testing is proceeding nicely.
        Firmware development and multi-crate testing in FY11
  16 Channel LE Discriminator/Scaler (Hall B requirement)
    7 ‘production’ units under test now
  VXS Crate Specification  Order should be awarded before Oct-10
  GTP  Scott Kaneta joins the group! GTP slips to FY11
  TS  Specified, and planned for FY11-FY12
Baseline Improvement Activities (BIA) review on 17-September
FY11 will be an intensive year of significant ‘system’ level testing to assure
that these boards are ready for final production quantity orders in early FY12
20

## Slide 30
Level 1 & Trigger Distribution
Up to 128 front-end crates
CPU
VXS-Crate
Global Trigger Crate
Trigger Distribution Crate
Trigger Decisions
L1 Subsystem Data Streams (hits & energy)
Fiber Optic
Links
SSP can manage
8 CTP
(Crates)
Front-End Crates
VME Readout to Gigabit Ethernet
TI
SSP
SSP
SSP
SSP
SSP
SSP
GTP
GTP
SSP
SSP
SSP
SSP
SSP
SSP
CPU
VXS-Crate
TS
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
Clock
Trig1
Trig2
Sync
Busy
Fiber Optic
Links
TD can manage
8 TI
(Crates)
13

## Slide 31: Synchronized Multi-Crate Readout
CTP #2 is also acting as an SSP (by summing the local crate + CTP#1 sum over fiber
A programmable threshold is set in CTP, which creates a trigger when the global sum (6 FADC boards => 96 channels) is over threshold.
Example test with a burst of 3 pulses into 16 channels across 2 crates/6 FADC modules
A 2μs global sum window is recorded around the trigger to see how the trigger was formed:
Example Raw Event Data for 1 FADC Channel:
B. Raydo

## Slide 32
Input Signal to 16 FADC250 Channels:
Raw Mode Triggered Data (single channel shown only):
Global Sum Capture (at “SSP”):
Runs at 250kHz in charge mode
Latency: 2.3µs(measured) + 660ns(GTP estimate) < 3µs
2 Crate Energy Sum Testing
Threshold applied to global sum (96 digitized channels) produces 3 triggers.
Raw channel samples extracted from pipeline shown for 1 channel.
B. Raydo

## Slide 33: Synchronized Multi-Crate Readout Rates
FADC event synchronization has been stable for several billion events @ ~150kHz trigger rate.
Have run up to 140kHz trigger rate in raw window mode, up to 170kHz in Pulse/Time mode.
Ed Jastrzembski has completed the 2eSST VME Interface on FADC allowing ~200MB/s readout
B. Raydo
Single Crate
12 signals distributed
to four FADC250
18% Occupancy