## Slide 1: Level 3 Trigger
Elliott Wolin
GlueX Upgrade Workshop
2-May-2012

## Slide 2: Outline
History and Pre-History
Current Understanding
Revisiting Strategy
Summary and Conclusions

## Slide 3: 1. History and Pre-History
My earliest reference is 1999 Design Report
  Original analysis and strategy from Dave Doughty
    Chapter 7 “Rates, Trigger and DAQ”
    Based on experience from CLAS
      higher-level hardware trigger expensive
      general-purpose computers cheap
    Skip custom hardware, go with online trigger farm 
    Dave called it a “Level 2” trigger then
      We complained and he eventually switched to “Level 3”
  Analysis performed by Dave D, Elton, Larry D and me

## Slide 4: History and Pre-History - 1999
 | Low Rate | High Rate
Event Size | 5 kB | 5 kB
Event Rate to L3 Farm | 10 kHz | 100 kHz
Data Rate to L3 Farm | 50 MB/s | 500 MB/s
Num Links | 20 | 20
Rate per Link | 2.5 MB/s | 25 MB/s
Link Technology | 100 MBit Ethernet | GBit Ethernet
Events/s/Link | 500 | 5000
Num Instr/Event for L3 | 1,000,000 | 1,000,000
Processing Power/Link | 500 MIPS | 5000 MIPS
Num 1000 MIPS Procs/Link | 1 | 10
Total 1000 MIPS Procs | 20 | 200

## Slide 5: History and Pre-History - 2002
 | Low Rate | High Rate
Event Size | 5 kB | 5 kB
Event Rate to L3 Farm | 20 kHz | 200 kHz
Data Rate to L3 Farm | 100 MB/s | 1000 MB/s
Num Links | 1 | 10
Rate per Link | 100 MB/s | 100 MB/s
Link Technology | GBit Ethernet | GBit Ethernet
Events/s/Link | 20000 | 20000
SPECints/Event for L3 | 0.1 | 0.1
SPECints/Link | 2000 | 2000
SPECints/Link x 2 | 4000 | 4000
Num 200 SPECint Procs/Link | 20 | 20
Total 200 SPECint Procs | 20 | 200

## Slide 6: History and Pre-History – 2008
 | Low Luminosity | High Luminosity
L1 trigger rate | 20 kHz | 200 kHz
Average event size | 15 kB | 15 kB
Date rate off detector | 300 MB/s | 3 GB/s
L3 rejection | None | Factor 10
Rate to storage | 300 MB/s | 300 MB/s

## Slide 7
ROC
ROC
ROC
ROC
ROC
ROC
E
MU
E
MU
E
MU
E
MU
E
MU
E
MU
Monitoring
Farm
No Rejection
E
MU
RAID
SILO in Computer Center
2 PB/year
50
ROCs
6
EMUs
6
EMUs
12
Monitoring
Nodes
1
EMU
16 TB
16 hrs
Event Builder
Crossbar
DAQ at Low Luminosity
300 MByte/sec
300 MB/s
300 MB/s
300 MB/s
300 MB/s
300 MB/s
300 MB/s

## Slide 8: 2. Current Understanding
Changes and concerns since 2008 for high luminosity
  VME backplane speed, ≤150 MB/s
    Might have to split crates
  L3 event classification @ 100 Hz/core
    Need 2000 cores, not 200, for 200 kHz event rate
    10x faster than current Pythia reconstruction rate
  Upgrade ROC-to-EMU network
    ROC network board to 10 Gbit (from 1 Gbit)
    Some concentrator switches won’t handle aggregate rate

## Slide 10
If backgrounds 30% larger, or 20 kB events
  Networks and switches ok
    10 Gbit Ethernet, Infiniband (40 Gbit)
  DAQ ok
    May need additional EMU’s @ $5k each
  Storage ok
    RAID and tape drives should handle rate

## Slide 11: 3. Revisiting Strategy
Skip L3, just write 200k events/sec to tape?
  Analysis by Dave Lawrence and Sandy Philpott
  Data rate 3 GB/sec @ $10/TB storage
    $300k/year for tapes, no backup
    Tapes currently 3x more expensive
  Tape silo
    Would need 1-2 additional silos @ $250k each no backup
    Assumes data in silo 4 years
  Some network upgrades
    Infiniband or 10GBit Ethernet or ???

## Slide 12: Revisiting Strategy
Compare to L3 trigger strategy
  $200k for the L3 farm
    2000 cores @ $100/core

## Slide 13: 4. Summary and Conclusions
Original strategy still optimal
Event size, data rates, cpu req’s have increased
Computing and network costs keep decreasing
Overall L3 design easily scalable
  Robust against increased data rate
At most might need to
  Split VME crates
  Add few EMU’s
  Upgrade some network connections

## Slide 14: Backup

## Slide 15
Detector
Level 1
Energy Sum
Trigger
Trigger
Supervisor
Module
T
r
igger
Inputs
Add’l
Trigger
Logic
O
u
t
p
u
t
Pulser 1
Pulser n
Calib 1
Calib n
Trigger Signal
Full Experiment Trigger
16 bits
16 bits