## Slide 1: DAQ Status & Plans
GlueX Collaboration Meeting – Feb 21-23, 2013
Jefferson Lab
Bryan Moffit/David Abbott

## Slide 2: Overview
FCAT
Current Status Update
  CODA3, Hall D tasks etc…
DAQ Test Stand
  Counting House setup
  Timeline, Testing plans
Summary

## Slide 3: FCAT
Full Crate Acceptance Test
  Requires: CODA 2.6.2, ROOT, Recent Module drivers
  Currently reuses FP-SD, CTP, Controller
Hardware setup
  Set fADC250 VME Addresses, JTAG dips, Channel Ranges
  Install modules in crate
  Cable up Power, Ethernet, and Trigger Connections
  Power on and Set Crate Fan Speed

## Slide 4: FCAT
Software Tests:
  CRATESCAN
    Identify all modules in crate (VME addr, serial numbers)
    Update firmware, if needed
  PEDESTAL
    No inputs, random pulser trigger
  PAYLOAD1 (~4 kHz trig2, blocklevel = 1)
    Simple programmed payload into ALL channels
  PAYLOAD2 (~4 kHz trig2, blocklevel = 2)
    Simple programmed payload into One channel/module
  RATETEST (~150 kHz trig2, blocklevel = 100)
    Same as PAYLOAD2

## Slide 5: Current Status
Still 2 supported releases (through startup of 12GeV)
  CODA 2.6.2 (standard operational release)
    NO: Event Blocking, EVIO Version 4 files
    End of Life – no further development – only support
  CODA 3.0 (currently Beta)
    NO: EVIO Version 1 files, vxWorks ROCs
    Under rapid development – changes are frequent
New useful Tools developed for CODA 3 configuration and monitoring:
  Jcedit - COOL Run Configuration editor
  Jeviodmp – EVIO v4 file viewer
CODA 3 developments are at a point where availability of all the new hardware in a large data acquisition test stand is highly desired to work out many details/features/bugs!

## Slide 6: VME CPU status…
VME CPU procurement was only partially completed this fall.
  New 3rd gen Intel Core i7 boards did not initially pass our low level VME tests (it has since been resolved).
  A small order of 2nd Gen boards were ordered to cover near term needs (Hall D ordered 7).
GE Intelligent Platforms won the bid (~1K/CPU cheaper) over Concurrent Technologies.
A final PO for the remainder of boards can happen when desired (anytime this fiscal year)
A final technical note: Concurrent boards support direct VXS (PCIe) high-speed access to switch slot boards (ie CTP,GTP). This may be useful in some crates (L1 trigger).

## Slide 7
COOL Configuration Editor (jcedit)
Component
Classes
Defined
components
Configuration
Layout
(double-click icon
to get component
details)

## Slide 8: Run Control GUI
User interface to DAQ including:
Control buttons
Config parameters
Run Status
Component status
Event/Data Rates
System messages

## Slide 9: Jevio Event Dump Utility (jeviodmp)

## Slide 10
Hall D Online tasks for DAQ Group
Projects “completed”:
Design framework and prototype Hall D Farm monitoring architecture
  (AFECS-based Process and Hardware monitoring/control Agents available)
  Create DAQ-like EVIO files from Monte Carlo data (mc2coda library)
Projects in various stages of development:
Self-configuring readout list with database storage of crate configurations
  Event disentangler tailored for Hall D crates
  Top Level Experiment control system supervisor and GUI
  Trigger Config/Control System and GUI
ALL of the projects still under development will benefit greatly from a
non-trivial DAQ Test Stand (i.e. more than a few crates, all new hardware available for use)

## Slide 11
GlueX DAQ System
~20% slice
of total system

## Slide 12: DAQ Test Stand
Prior efforts
  Many parts of DAQ system tested individually in small test stands
  DAQ group unable to perform large-scale tests
    Never had enough equipment/space
Why test “slice” of full DAQ now?
  Software/Hardware developments have matured.
  Hall D has all the necessary equipment
  Computing system available soon
    Some hardware can be borrowed from CC and HPCC
  Rack Room LHS is not in use – plenty of empty racks & power
  Benefit to both DAQ/Electronics groups and they have manpower
  DOE review this summer may focus on DAQ readiness

## Slide 13: DAQ Test Stand – Timelines & Goals
Rack Room ready now (all necessary power 110 & 208)
Computing equipment (CPUs, switches, cabling etc…) is currently being installed.
Plan to have a total of 12 crates (10 ROCs, TS, and Global Trigger crate). As crates are filled and tested by Fernando’s group they will be installed in the rack room. Should have all by early April.
Testing will include:
  Performance testing with complex configs (multi-stage event building, asymmetric data streams).
  Trigger/clock distribution, long-term stability, error detection, calibration and recovery.
  Develop DAQ system partitioning with the TS
  Much more…

## Slide 14: Rack Room Setup
Control Room
(Misc PCs and Consoles)
R1
R2
R10
R5
R4
R3
R11
R6
R7
R8
R9
R12
R13
R14
R15
R16
R17
R18
EMU
Nodes
Main
Ethernet
&
IB
Switches
RAID
Disks
2 VXS
1 TS crate
3 VXS
3 VXS
2 VXS
1 Global Trig
Terminal Server,
NIM, Ethernet
10 Gb Uplink
Misc
DAQ
CPUs
L3
Farm
Nodes
ROCS

## Slide 15: Summary
The various pieces of CODA 3 are progressing. We are at a point where integration of these components is possible -and essential.
We have all the necessary hardware to pull together a large DAQ test stand in the Hall D Counting house. We hope to keep this system in place through the fall.
As Detector systems are installed in the Hall we will be able to integrate them into the DAQ system.
Both Hall-based DAQ and the Rack room system will be able to run at the same time.