## Slide 1
David Lawrence JLab
May 9, 2016
Hall-D Online Systems Status
(special guest appearance by L3 trigger status)

## Slide 2
554.3TB

## Slide 3: Data Rates
ROC
Event Builder
Event Recorder
Tape Library
ROC
ROC
ROC
ROC
ROC
ROC
ROC
Spec: 100MB/sec
Tested: ~30MB/sec
Spec: 3000MB/sec
Tested: 600MB/sec
Spec: 300MB/sec
Tested: 600MB/sec
Spec: 300MB/sec
Tested: 450MB/sec
“Tested” means with actual data while it was being acquired. In some cases, offline testing has achieved significantly higher rates.
72TB x2
RAID disk
(L3 farm)
125.9TB in 147,355 files written to tape in 2014 commissioning run
800MB/sec
800MB/sec
2000MB/sec

## Slide 4: Online Storage Capacity
Two RAID disks with 72TB each of usable space
  Maintain some portion of recent data
  ~100TB effective space total for new data
Need 72hr buffer in case of issue with link to tape library
100TB ÷ 800MB/s = 35hr
Need additional 100TB of RAID
  Will purchase this summer

## Slide 5: Event Size vs. Beam Current
Slope = 1kB/nA
extrapolate to Ibeam= 0  14.25kB/event
Event Size: ~19kB
Accidental data fraction (by volume):
100nA: 26% of data is due to accidentals
200nA: 41% of data is due to accidentals
5.0mm collimator
(0.05kB/nA)(Ibeam nA)
(0.05kB/nA)(Ibeam nA) + (14.25kB)

## Slide 6: L3 Testing
ET
EB
ET
ER
L3
L3
L3
gluon100
gluonraid1
Primarily infrastructure testing done
Limited by 12 node farm to ~200MB/s parsing rate
(~10kHz input rate)
(Goal: Reduce data volume by factor of 10)
Spring 2016 L3 Testing

## Slide 7
32 parsing threads
32 processing threads
4 parsing threads
32 processing threads

## Slide 8: Reconstructed parameters for old and new parsers

## Slide 9
Will be purchasing additional 8 farm nodes this year which should be roughly 2x as fast as existing ones
(farm capacity will increase roughly 2.3x)

## Slide 10
Will be purchasing additional 8 farm nodes this year which should be roughly 2x as fast as existing ones
(farm capacity will increase roughly 2.3x)

## Slide 11
Will be purchasing additional 8 farm nodes this year which should be roughly 2x as fast as existing ones
(farm capacity will increase roughly 2.3x)

## Slide 12: Online Monitoring
RootSpy system crushed under weight of successful campaign to create histograms
  O(104) histograms being filled and passed around
  Non-responsive interface resulted in unusable online monitoring system
Replaced all plugins with single plugin that defines <40 histograms
Added HDMONITOR e-log and button to make logbook entry

## Slide 14: Example Plots from RootSpy

## Slide 15: Password for Hall-D Operations Account
Do not write passwords on whiteboards
Do not send passwords in e-mails
Do not write passwords in scripts (especially ones kept in repositories that can be seen from web)
Do not write passwords on wiki (or any other web page)
Hall-D Operations password must be obtained via word of mouth (contact Run Coordinator if needed)

## Slide 16: Backups