## Slide 1: The GlueX Start Counter & Beam Asymmetry in Single Photoproduction Eric Pooser Dissertation Defense Advisor: Werner Boeglin 03/25/2016

## Slide 2: Nuclear & Particle Physics
Eric Pooser
Dissertation Defense
March 25, 2016
Primary goals:
  Study the structure of matter in the universe
  Study the fundamental forces existing in nature
Standard Model: explains how the basic building blocks of matter interact, governed by four fundamental forces
Elementary particles: building blocks of matter
  Quarks: building blocks of hadrons
  Leptons: substructure unknown
Force carriers: quanta of gauge fields
  Electromagnetic: γ
  Strong nuclear: g
  Weak nuclear: W+, W–, Z
Higgs boson: Higgs field excitation
  Particle masses arise from field interaction
MATTER
FERMIONS
BOSONS
FORCE CARRIERS
LEPTONS
QUARKS
HIGGS BOSON
GAUGE BOSONS

## Slide 3: Hadronic Matter
Eric Pooser
Dissertation Defense
March 25, 2016
Hadrons: Particles comprised of quarks bound by gluons
Baryons (Antibaryons):
Mesons:
Tetraquarks (Or bound mesons?):
  Recent candidates: ZC(3900), Z(4430) ...
Hybrid mesons?
  Several candidates, none unambiguous
Pentaquarks? Glueballs?

## Slide 4: Classification of Mesons
Eric Pooser
Dissertation Defense
March 25, 2016
General properties: mass, charge, quark flavor
Grouped by quantum numbers:
  Total angular momentum:
  Parity: Spatial inversion
  Charge: Charge conjugation
Allowed for system:
  , , , , …

## Slide 5: Classification of Mesons
Eric Pooser
Dissertation Defense
March 25, 2016
General properties: mass, charge, quark flavor
Grouped by quantum numbers:
  Total angular momentum:
  Parity: Spatial inversion
  Charge: Charge conjugation
Allowed for system:
  , , , , …

## Slide 6: Hybrid & Exotic Hybrid Mesons
Conventional light mesons (π, K, η, ρ, ω, φ, …)
  system (q = u, d, or s)
  Gluonic degrees of freedom do not contribute
  Non-exotic quantum numbers:
Hybrid Mesons: Resonances with gluonic field excitations
  Gluons behave as constituent particle
  Provide access to gluonic degrees of freedom in the confinement regime
Exotic Hybrid Mesons: Hybrid mesons with non-permissible quantum numbers
  Exotic quantum numbers:
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 7: Lattice QCD Predictions
Rich spectrum of light quark & quark-gluon hybrid (exotic) mesons
Eric Pooser
Dissertation Defense
March 25, 2016
J. Dudek, et al., Phys. Rev. D 88, 094505 (2013)
Lightest Hybrid Mesons
Negative Parity
Exotics
π1
Positive Parity

## Slide 8: Hints of Exotic Mesons
E852 Collaboration (BNL)
  18 GeV/c π- beam, LH2 target
Eric Pooser
Dissertation Defense
March 25, 2016
COMPASS (CERN)
  190 GeV/c π beam, Pb target
E.I. Ivanov, et al., PRL 86, 3977 (2001)
M.G. Alekseev, et al., PRL 104, 241803 (2010)
Exotic π1(1600)

## Slide 9: Jefferson Lab & GlueX
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 10: Jefferson Lab & GlueX
Jefferson Lab CEBAF Accelerator
  Injector: 3 independent 500 MHz polarized electron beams
  e– beam: Upgraded from 6 to 12 GeV
    Up to 5.5 passes through 2 superconducting linacs (∼1500 MHz at K )
  Parallel delivery of beams to 3 Halls
GlueX experiment: New experimental hall D, designed to search for hybrid & exotic mesons
  GlueX collaboration: ~110 members, 23 institutions
  Other physics: Map baryon spectra, charged pion polarizability, rare eta decay, etc.
  Commissioning: Fall 2014 – April 2016
  First physics running: Fall 2016
  Full intensity: 2017+: ~5 years
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 11: CEBAF at Jefferson Lab
Eric Pooser
Dissertation Defense
March 25, 2016
A
B
C
D
CHL

## Slide 12: Experimental Hall D
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 13: Hall D
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 14: GlueX Beamline
Eric Pooser
Dissertation Defense
March 25, 2016
12 GeV e- beam (0.05 – 2.2 μA)
20 μm thick diamond radiator
  8.4-9.0 GeV γ’s in the coherent peak
    3.0-11.8 GeV tagged
  ~40% linearly polarized γ’s
  Collimated r < 1.8 mm at ~80 m
  100 MHz γ’s at 2.2 μA
9 GeV Coherent Peak

## Slide 15: GlueX Beamline
Eric Pooser
Dissertation Defense
March 25, 2016
12 GeV e- beam (0.05 – 2.2 μA)
20 μm thick diamond radiator
  8.4-9.0 GeV γ’s in the coherent peak
    3.0-11.8 GeV tagged
  ~40% linearly polarized γ’s
  Collimated r < 1.8 mm at ~80 m
  100 MHz γ’s at 2.2 μA
~35% Peak Polarization

## Slide 16: GlueX Spectrometer
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 17: The GlueX Start Counter
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 18: Start Counter with Beam Line & Target
Eric Pooser
Dissertation Defense
March 25, 2016
EJ-200 scintillator material with a decay time of 2 ns and a long attenuation length
Magnetic field insensitive SiPM detectors comprise the readout system
In coincidence with the tagger the ST identifies accelerator beam buckets ~ 4 ns apart
Designed to operate at tagged photon rates of up to
to successfully identify beam buckets with a high degree of accuracy
segmentation for background rejection

## Slide 19: Start Counter Readout System
10 ST1 Boards, houses 30 groups of 4, 3x3 mm2 SiPMs
Read out 30 scintillator paddles
3 x 12 mm2 active area
≈72 % of scintillator area is readout at upstream end
ST3
Fully Assembled Readout System
ST1 & SiPMs
Support Hub
ST2
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 20: Start Counter Detector System
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 21: Testing Machined Scintillators
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 22
Eric Pooser
Dissertation Defense
March 25, 2016
Test Stand

## Slide 23
Eric Pooser
Dissertation Defense
March 25, 2016
Test Stand

## Slide 24: Polishing Machined Scintillators
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 25: Polishing Methods
Workers at McNeal Enterprises badly damaged scintillator surfaces
Buehler Micropolish II de-agglomerated Alumina suspension (0.3 μm)
Polishing times were ~1 hr per paddle
With the combination of wet, cold buffing, and hand polishing, the scintillators were made void of virtually all scratches and surface defects
Polishing procedures greatly improved the performance of the scintillators
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 26: Effects of Polishing Scintillators
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 27: Start Counter Paddle Results (Wrapped)
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 28: GEANT4 Simulations
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 29: Experimental Setup
Goal was to understand the light collection in the nose region
The two trapezoidal regions of machined scintillator were modelled
  Wide straight sections & tapered nose section
EJ200 scintillator material was modelled with only one parameter
  Reflectivity of G4LogicalSkinSurface = 98%
  SiPM constructed as G4SensitiveDetector made of Silicon with 100% detection efficiency
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 30: Experimental Setup
10K Optical photons were generated
  16 Different locations inside the scintillator medium
  Energies between 0.5 eV – 3.0 eV
  Generated randomly in 4 along a 3 mm path (y-axis)
  Orthogonal to wide surface of the scintillator
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 31: Results
Eric Pooser
Dissertation Defense
March 25, 2016
Factor 1/2 light loss
Factor 3/2 light gain

## Slide 32: Start Counter Assembly
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 33: Assembly Jig
Eric Pooser
Dissertation Defense
March 25, 2016
Scintillator
Rohacell
Acrylic Ring (x2)
Foam (x62)
Swivel Screw (x60)
Pneumatic Cylinder (x2)
SiPM (x30)
Support Hub
CMOS Color Camera
12 deg Locking Rotation Device
Mounted Steel Ball Bearings (x2)
Locking Plunger

## Slide 34: Assembly Jig
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 35: Shimming Procedure
Both the scintillator and the active area of the SiPM are 3 mm
  Proper alignment was required to maximize light collection
SiPM’s were positioned so that all paddles would require 30 mils (762 μm) of radial shimming
  Material utilized was Kapton polyimide heavy duty film (type HN ρ = 1.42 g/cc), cut into 0.5 x 12 in2 strips
  5, 10, & 20 mil Kapton sheets were utilized
The required shimming height varied from paddle to paddle
    20 mil < shim < 40 mil
Utilizing a calibrated camera we were able to measure distances with very high precision (< 10 μm)
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 36: Shimming Procedure
Camera
Scintillator
0.8 mil Bundling Wrap
Rohacell
Rings & Swivel Screws
Hub
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 37: Calibration Measurement (3.02 mm)
1 pixel = 1 mil
Rohacell
SiPM
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 38: No Shimming (786 μm Needed)
Scintillator
Bundling Wrap
1 pixel = 1 mil
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 39: 10 mil Shimming (507 μm Needed)
1 pixel = 1 mil
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 40: 20 mil Shimming (254 um,1 pixel = 1 mil)
1 pixel = 1 mil
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 41: 25 mil Shimming (152 um,1 pixel = 1 mil)
1 pixel = 1 mil
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 42: 30 mil Shimming (Best Possible Alignment)
1 pixel = 1 mil
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 43: Scintillator & SiPM Air Gap (1.9 mm)
1 pixel = 40.5 μm
Scintillator
SiPM
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 44: Scintillator & SiPM Air Gap (Spacer Thickness ≈ 150 μm)
Spacer Material
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 45: Scintillator & SiPM Air Gap (162 μm)
1 pixel = 40.5 μm
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 46: Fully Assembled Start Counter (EEL 126)
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 47: Time Walk Corrections
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 48: Time Walk Corrections
Eric Pooser
Dissertation Defense
March 25, 2016
Pulse peak is utilized to characterize the leading edge
  ≡ time walk correction function
  ≡ pulse amplitude
  ≡ most typical pulse height for ith paddle
  ≡ discriminator threshold (converted to ADC units)
  Spring 2015 runs 2931-2934 (≈ 81.5 M events)
  50 nA, 5.5 GeV, 800 A, LH2, 5.0 mm collimator
  50 Diamond radiator

## Slide 49
Eric Pooser
Dissertation Defense
March 25, 2016
Time Walk Corrections
For each pulse peak bin ranging from 50 to 2100 channels, the corresponding δt () projection is fit with a Gaussian
  μ FWHM*σ
Each , with errors determined from the fit, are then plotted against its respective pulse peak value
ROOT’s minimization library Minuit is then utilized to perform the fit
Projection

## Slide 50: Attenuation Corrections
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 51
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
The ADC peak & pedestal were isolated by cutting on the TDC spectrum
  In time: Peak
  Out of time: Pedestal
For each source location the ADC peak & pedestal were fit
  The means are extracted and subtracted to obtain the true ADC values for each source location
ADC Pedestal
Channel 1
z = 32.36 cm
Channel 1
z = 32.36 cm
ADC Peak
ADC Pedestal
Channel 1
z = 32.36 cm
CFD

## Slide 52
Eric Pooser
Dissertation Defense
March 25, 2016
Pedestal corrected ADC means are then plotted vs. 90Sr source distance along paddle
The data are fit to two different regions of each paddle
  Straight section:
  Bend/Nose Section:
The correction is calculated by the following method:
  Straight Section:
    Where:
  Nose Section:
    Where:
Attenuation Corrections (Bench Data)

## Slide 53
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)

## Slide 54
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
Uncorrected dE/dx vs. P in the Start Counter
p
π, e, K

## Slide 55
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
Corrected dE/dx vs. P in the Start Counter
p
π, e, K

## Slide 56: Propagation Time Corrections
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 57
Eric Pooser
Dissertation Defense
March 25, 2016
Developed method for acquiring a reference time that is external of the ST
Event Selection (Run 2931)
  Charged tracks with best tracking FOM (FOM > 3σ)
  50.0 cm < zvertex < 80.0 cm
  rvertex < 3.745 cm (scattering chamber radius)
Track matched to the TOF
  Does not also have a match to the ST
  π- tracks with p > 0.5 GeV
  Calibrated TOF hit time is propagated back to the vertex and corrected for the RF time
    Serves as single reference time for all tracks matched to the ST in that event
Tracks matched to the ST
  Hit times are time-walk & flight time corrected
Time difference (TOF & ST) and z intersection with ST are recorded
Propagation Time Corrections (Beam Data)

## Slide 58
Eric Pooser
Dissertation Defense
March 25, 2016
Only 5 mm wide bins in z that have more than 65 entries were considered
  Gaussian fit, mean and error extracted
Functional forms are fit to the straight, bend, & nose regions
  Initial round of fits are performed to offset all values so the y-intercept of the straight section is 0.0
  This allows one to calculate the time difference explicitly
Clear deviation from constant effective velocity correction
The corrections are as follows
Propagation Time Corrections (Beam Data)

## Slide 59: Time Resolution Measurements
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 60
Eric Pooser
Dissertation Defense
March 25, 2016
Time Resolution Measurements
To calculate time resolution of the Start Counter one must calculate the time difference of two quantities:
  Calibrated ST measure of the target time:
  Shifted RF time (corrected for photon propagation to vertex of track) matched to ST hit time
Straight
Bend
Nose
Total

## Slide 61
Eric Pooser
Dissertation Defense
March 25, 2016
Propagation Time Corrections (Beam Data)
Average Performance Resolution
0.290 0.001 ns
Design Performance Resolution
0.350 ns
All Sections
ST Section | σall | σstraight | σbend | σnose
σavg | 290 ps | 299 ps | 292 ps | 264 ps
Overall Improvement in the Nose

## Slide 62: Beam Asymmetry in Single Photoproduction
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 63
Aim to measure the polarization observable (beam asymmetry) by investigating the photoproduction of mesons utilizing 2.5 – 3.0 GeV linearly polarized photons and the -bin method technique
  Single polarization observables aid in determining the properties of the nucleon resonance spectrum [1]
  Offer important constraints on photoproduction reactions [1]
can be extracted as the amplitude of the modulation of the meson, corrected for the degree of polarization
  is determined from a fit to the coherent peak
  The dependence of arises from the partial wave expansion of the helicity amplitudes
Eric Pooser
Dissertation Defense
March 25, 2016
Outlook
  [1] = M. Dugger, et. al. (CLAS): PRC 88, 065203 (2013)

## Slide 64
order event selection
  Combos of 2 ’s and 1 were reconstructed
  Reject all beam photons that match to a different RF bunch
  > 100 MeV in FCAL & BCAL
1st order event selection
  PID cuts (Detector measure of track/shower vertex time)
  Proton candidates
    = 1.0 ns in BCAL & TOF
    .0 ns in FCAL
  candidates
    = 1.5 ns in BCAL
    .0 ns in FCAL
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 65
PID dE/dx cuts in CDC
  Empirical exponential function utilized to minimize /e/K contamination
  Better at maximizing number of “good” proton candidates rather than imposing a horizontal (constant) dE/dx cut
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection
BEFORE
AFTER

## Slide 66
Vertex cuts
  Require that recoil proton have vertex contained within target geometry
5 mm 50 cm 80 cm
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 67
Kinematic Cuts
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 68
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 69
Coherent peak cut (PARA Orientation)
Fit to enhancement spectrum yields a measure of both the maximum and average beam polarization
  Determined by K. Livingston in which he fit the coherent peak for runs 3185 & 3186
Eric Pooser
Dissertation Defense
March 25, 2016
Coherent Peak & Beam Polarization

## Slide 70
distribution of the is fit with the following function:
  where
Cross section is given by:
distribution of shows no asymmetry for amorphous runs
  Run 3180 (~41 M events)
distribution of shows clear modulation for PARA runs
  Runs 3185 & 3186 (~33 M events)
Eric Pooser
Dissertation Defense
March 25, 2016
Azimuthal Asymmetry

## Slide 71
Eric Pooser
Dissertation Defense
March 25, 2016
Azimuthal Asymmetry
Measured in 3 bins of Mandelstam t
Similar measurements were conduced by Bellenger et al. at MIT 46 years prior at CEA
  PRL 23, 240 (1969)
  8 bins in
  This comprises the world data set

## Slide 72
After only two hours of physics production data the GlueX data is remarkably similar to that of the CEA data set
Errors in do not take into account the error in the avg. polarization
  Possibly a ~10% effect
Eric Pooser
Dissertation Defense
March 25, 2016
Beam Asymmetry

## Slide 73
The GlueX Start Counter has performed well under design resolution during the commissioning runs (Fall 2014 – Present)
  No signs of deterioration have been observed to date
The world data set of the beam asymmetry polarization observable in single photoproduction was matched utilizing the GlueX spectrometer
  Only 2 hours of physics production data were collected
GlueX will provide a wealth of physics for the next 10+ yrs
Eric Pooser
Dissertation Defense
March 25, 2016
Summary

## Slide 74: Backup Slides
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 75: Current Hall-D Physics Program
Eric Pooser
Dissertation Defense
March 25, 2016
Slide Courtesy of E. Chudakov

## Slide 76
Charged-π Polarizability in
  : Electric Polarizability
  : Magnetic Polarizability
  Measure:
  via. Primakoff production
via. the Primakoff Method
  Determination of the light quark mass ratio
  Measure mixing angle
Eric Pooser
Dissertation Defense
March 25, 2016
Approved Experiments in Hall D

## Slide 77: Fall 2014 GlueX Commissioning Status
~10.1 GeV e- beam, 50 - 200 nA
  CH2 target
  800-1200A solenoid current
  ~ 19 days of integrated beam (post-beam tune)
GlueX Commissioning Goals:
  Tune CW beam to tagger 
  Create unpolarized γ beam and tune through collimator, target, and photon beam dump 
  Checkout trigger, DAQ, and all detector subsystems 
  Collect data for initial detector calibration & DC alignment 
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 78: Fall 2014 GlueX Physics Results
A few reconstructed decays:
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 79: Spring 2015 GlueX Commissioning Status
  ~5.5 GeV e- beam, 5 - 200 nA
  800-1300A solenoid current
  ~10 days of beam (post-beam tune)
Commissioning Goals
  Polarized γ beam (goniometer & diamonds) 
  LH2 cryotarget & verify alignment 
  Run DAQ in block-mode at high rates 
  Optimize triggers 
  Beam stability feedbacks ~ (more work is needed)
  Accelerator RF timing 
Solenoid was stable at 1200A for ~3 weeks
  1 day of running at 1300A caused a quenched
  Reviewed by Physics Division on July 14, 2015
  No obvious cause of the quench has been identified
  Support plans to run at 1300A again
All equipment for the baseline GlueX detector has been commissioned!
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 80: Polarized Photons
50 & 100 μm (Hall-B) thick diamonds were scanned and aligned
Photon polarization is understood and can be controlled
Both produced coherent radiation!
Eric Pooser
Dissertation Defense
March 25, 2016
Coherent Edge

## Slide 81: Photon Beam Diagnostics
Eric Pooser
Dissertation Defense
March 25, 2016
Tagger Hodoscope
Pair Spectrometer
Triplet Polarimeter
Tagger Microscope

## Slide 82: Track/Vertex Reconstruction
Reconstruction of charged track vertices during Spring run
Target, scattering chamber, & start counter geometries can be observed
Particle tracking and reconstruction is at a mature level
Eric Pooser
Dissertation Defense
March 25, 2016
Target Empty
Target Full

## Slide 83: Event Display/Track Reconstruction
Eric Pooser
Dissertation Defense
March 25, 2016
CDC
CDC
BCAL
BCAL
FDC
FDC
Slide Courtesy of P. Mattione

## Slide 84
Eric Pooser
Dissertation Defense
March 25, 2016
TOF
FCAL
BCAL
CDC
CDC
BCAL
CDC
BCAL
FDC
FDC
Event Display/Track Reconstruction
Slide Courtesy of P. Mattione

## Slide 85: Offline/Online Monitoring
Bi-weekly “launches” run over all available data on tape and reconstructed data is written to disk for physics analyses
Web run browser provides ability to browse and download ROOT files:
  https://halldweb.jlab.org/cgi-bin/data_monitoring/monitoring/runBrowser.py
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 86: PID Capabilities
Eric Pooser
Dissertation Defense
March 25, 2016
TOF
TOF
CDC
FCAL

## Slide 87: Tracking & Calorimetry Performance
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 88: Mass Peaks in Exclusive Reactions
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 89: Polarization Transfer in ρ Production
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 90: Future GlueX PID Upgrade (FY18)
Improved π/K separation (up to 4 GeV) extends physics program to study mesons and baryons containing strange quarks
Received approval from SLAC to use BaBar DIRC components
  48 fused silica bars contained in 4 boxes
Implementing a compact, focusing optics system
Synergy with CLAS12 RICH MaPMT readout and electronics
  ~15K readout channels integrated into standard Hall D DAQ system
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 91: Backup Slides
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 92: GlueX Detector System
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 93: Lattice QCD Predictions
Eric Pooser
Dissertation Defense
March 25, 2016
Lightest Hybrid Mesons
Negative Parity
Positive Parity
Exotics
π1
J. Dudek, et al., Phys. Rev. D 88, 094505 (2013)

## Slide 94: Exotic Hybrid Meson Decay Channels
GlueX designed to reconstruct all of these decay channels
Eric Pooser
Dissertation Defense
March 25, 2016
P. R. Page, E. S. Swanson and A. P. Szczepaniak, Phys. Rev. D 59, 034016 (1999). mπ = 396 MeV/c2

## Slide 95: Approved Experiments in Hall D GlueX
Map spectrum of light quark & quark-gluon hybrid (exotic) mesons
Study meson & baryon decays to strange final states
GlueX: 21 Institutions, ~110 Scientists
Eric Pooser
Dissertation Defense
March 25, 2016
Exotic Hybrid Mesons

## Slide 96: DAQ
GlueX (now): DAQ 20 kHz, 300 MB/s tape
GlueX (physics running): DAQ 100 kHz, 1500 MB/s L3 20 kHz tape
Issues left to resolve:
  CODA: difficult to start, network issues
  Firmware: fADC-125 MHz, CAEN TDCs
  Long events due to low thresholds and noise issues
Spring 2015 results
  Stable at buffer/block level = 1 3 kHz at 50% live time, 200 MB/s
  Tests at buffer = 4 / block = 40 30 kHz at 97% live time, 600 MB/s
    Still unstable, crashes in approximately one minute
DAQ is still a work in progress
Eric Pooser
Dissertation Defense
March 25, 2016
Slide Courtesy of E. Chudakov

## Slide 97
Precise measurement of the charged pion polarizability will be conducted by measuring via. Primakoff production
ChPT predicts that the electric () & magnetic () charged pion polarizabilities are related to their respective weak form factors &
Tests fundamental symmetries in the intrinsic even-parity sector of QCD
Reduces uncertainty in the SM prediction of
Eric Pooser
Dissertation Defense
March 25, 2016
Approved Experiments in Hall D Charged Pion Polarizability in

## Slide 98
Extract mixing angle
Determination of the light quark mass ratio
Eric Pooser
Dissertation Defense
March 25, 2016
Approved Experiments in Hall D via. the Primakoff Method

## Slide 99: Approved Experiments in Hall D GlueX
Map spectrum of light quark & quark-gluon hybrid (exotic) mesons
Study meson & baryon decays to strange final states
GlueX: 21 Institutions, ~110 Scientists
Hall D: 13 Staff Scientists, 1 Post Doctorial Fellow
Eric Pooser
Dissertation Defense
March 25, 2016
Exotic Hybrid Mesons

## Slide 100: (958) Photoproduction %
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 101
Aim to isolate the decay channel
  Including non-resonant
  Spring 2015 data (golden runs): 2931, 3079, 3179, 3180, 3182, 3185, 3186
Many studies were conducted utilizing “poor-man” kinematic cuts
  Virtually impossible to isolate production with Spring 2015 Data
order event selection
  Combos of 2 ’s, 1 , and 1 were reconstructed
  Reject all beam photons that match to a different RF bunch
  > 100 MeV in FCAL & BCAL
Loose pre-kinematic fit cuts
  Fiducial PID t cuts final state q’s
  Empirical exponential CDC dE/dx cut
Cut on kinematic fit confidence level > 0.1
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 102
  Require exactly 1 reconstructed shower in each event
Eric Pooser
Dissertation Defense
March 25, 2016
Event Selection

## Slide 103
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 104
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 105
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 106
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 107
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 108
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 109
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 110: Current Hall-D Physics Program
Eric Pooser
Dissertation Defense
March 25, 2016
Slide Courtesy of E. Chudakov

## Slide 111
Charged-π Polarizability in
  : Electric Polarizability
  : Magnetic Polarizability
  Measure:
  via. Primakoff production
via. the Primakoff Method
  Determination of the light quark mass ratio
  Measure mixing angle
Eric Pooser
Dissertation Defense
March 25, 2016
Approved Experiments in Hall D

## Slide 112: Initial Scintillator Performance (Unwrapped)
Average, Middle of Bend (42 cm), Tip of Nose (59 cm)
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 113: Polished Scintillator Performance (Unwrapped)
Average, Middle of Bend (42 cm), Tip of Nose (59 cm)
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 114: Start Counter Paddle Results (Wrapped)
Weighted Average σtr, Worst σtr, Best σtr
Eric Pooser
Dissertation Defense
March 25, 2016

## Slide 115
Eric Pooser
Dissertation Defense
March 25, 2016
Time Walk Corrections
Custom fit produces slightly better self timing resolutions than default ROOT fitter
Fitting algorithms can be easily modified to adjust fitting procedures without much overhead

## Slide 116
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
For each location the ADC spectrum and pedestal are fit
The means are extracted and subtracted to obtain the true ADC values for each source location
ADC Peak
ADC Pedestal
Channel 1
z = 32.36 cm

## Slide 117
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
The ADC peak & pedestal were isolated by cutting on the TDC spectrum
  In time: Peak
  Out of time: Pedestal
For each source location the ADC peak & pedestal were fit
  The means are extracted and subtracted to obtain the true ADC values for each source location
ADC Peak
ADC Pedestal
Channel 1
z = 32.36 cm
Channel 1
z = 32.36 cm
Channel 1
z = 32.36 cm

## Slide 118
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
Bench data taken at FIU utilizes a custom test stand which allows for a 90Sr source to be placed at 12 discrete locations along the path in the scintillator
  4 locations in the straight section (~ 10 cm apart)
  3 locations in the bend section (~ 1.3 cm apart)
  5 locations along the nose section (~ 3 cm apart)
  90Sr produces minimum ionizing electrons (0.5 – 2.5 MeV)
Trigger PMT provides reference time
QADCs & CFDs were utilized
Both ADC and TDC data were collected for all 30 paddles with the 90Sr source in the same 12 precise locations

## Slide 119
Eric Pooser
Dissertation Defense
March 25, 2016
Attenuation Corrections (Bench Data)
Example where the 5th order polynomial “explodes” for z < 10 cm
For this reason, two piecewise exponential functions are used
Over Correction
Under Correction

## Slide 120: Start Counter Detector System
Painted Rohacell
Tedlar
Wrapped Scintillator
Assembly Jig
Eric Pooser
Dissertation Defense
March 25, 2016