Neutral Particle Spectrometer

The neutral-particle spectrometer (NPS) offers unique scientific capabilities for studies the transverse spatial and momentum structure of the nucleon in Hall C. Five experiments have been fully approved by the JLab PAC to date (table 1), total of 160 PAC days approved: ~ 20% of all approved beam time in Hall C. E12-13-007: Measurement of Semi-inclusive π0 production as Validation of Factorization; E12-13-010: Exclusive DVCS and π 0 Cross Section Measurements in Hall C; E12-14-003: Wide-angle Compton Scattering at 8 and 10 GeV Photon Energies; E12-14-005: Wide Angle Exclusive Photoproduction of π0 Mesons; E12-17-008: Polarization Observables in Wide-Angle CS at large s, t and u; C12-18-005: Timelike Compton Scattering off a transversely polarized proton. Motivation of NPS Experiments: Validation of Reaction mechanism, to extract the rich information on nucleon structure encoded in GPD and TMDs one needs to show that the scattering process is understood. Combine NPS with Compact Photon Source (CPS) enables a gain of a factor of 30 in figure-of-merit. Enables a new suite of high-energy photon scattering experiments to image and understand the dynamical nucleon structure. Much progress in imaging nucleon structure can be made with electron-scattering reactions, yet experiments with high-energy photons play a unique complementary role. Small scattering probabilities of exclusive reactions demand high-intensity photon beams. Understanding strengthened by imaging longitudinally-polarized and transversely-polarized nucleons.
The Neutral Particle Spectrometer is ~25 msr neutral particle detector consisting of ~1080 PbWO4 crystals (30x36 matrix) in a temperature controlled frame including gain monitoring and curing systems. HV distribution bases with built in amplifiers for operation in a high rate environment. Essentially deadtime less digitizing electronics to independently sample the entire pulse form for each crystal, Jlab developed Flash ADC`s. A vertical-bend sweeping magnet with integrated field strength of 0.3 Tm to suppress an eliminate charged background. Cantilevered platforms off the Super High Momentum Spectrometer (SHMS) carriage to allow for remote rotation. For NPS angles from 6 to 23 degrees, the platform will be on the left of the SHMS carriage for NPS angles 23-57.5 degrees it will be on the right . A beam pipe with as large opening/critical angle for the beam exiting the target/scattering chamber region as possible to reduce beamline-associated backgrounds. Calorimeter conceptual design 30x36 (1080) PbWO4 crystals of size: 2x2x20 cm3 coupled with Hamamatsu R4125 PMTs with custom active HV bases. Design completed at IPN Orsay. Crystals will be placed in a 0.5 mm-thick carbon frame to ensure good positioning. PMTs will be accessible from the back side to allow for maintenance. Calibration and radiation curing with blue LED light though quartz optical fibers.

     Table 1
	E12-13-010	E12-13-007	E12-14-003	E12-14-005
Angular resolution(mrad)	0.5-0.75	0.5-0.75	1 - 2	1-2
Energy resolution(%)	(1-2)/√E	(1-2)/√E	5/√E	5/√E
Photon energies	2.6-7.6	0.5-5.7	1.1-3.4	1.1-3.4
Luminosity (cm-2cm-1)	~1038	~1038	~1.5x1038	~1.5x1038
Acceptance	60%/25msr	(10-60%)/25msr
Beam current(uA)	5-50	5-50	~40;+6% Cu radiator	~40;+6% Cu radiator
Target	10cm LH2	10cm LH2	10cm LH2	10Cm LH2