## Slide 1
Verification of the Pair Spectrometer Acceptance using
Compton events
(work progress)
Sasha, June 12, 2020

## Slide 2
For MC simulation set JANA_CALIB_CONTEXT to “variation = mc”
(for data processing use “variation = default “)
- CCDB tables with variation “mc” will be used during in Geant and mcsmear
Assigned variation “MC” to the beam_spot Monte Carlo table. Added PS acceptance to the CCDB
Some minor issues with the latest version of Geant 3
(inconsistency between the old and new geometries in digitization hitFTOF,
temporary fixed, need to do more tests)
Comments Regarding MC Simulation

## Slide 3
Start looking on runs with the smallest beam flux, 50 nA, He target
- uncertainties in the He target density (expected to be less that 5 %)
- small fraction of accidentals (in tagger and CCAL clusters). Try to check the shape of
Compton cross section
Event selection
- one cluster in the FCAL and one in the CCAL ( t = 8 ns ),  t (FCAL – RF) < 3 ns
- ECCAL > 1 GeV, EFCAL > 0.5 GeV
- fiducial cuts in calorimeters:
exclude fcal inner ring, -7 cm < XCCAL < 9 cm, -9 cm < YCCAL < 9 cm
Compton Reconstruction

## Slide 4
Monte Carlo Simulation: Compton Events
Monte Carlo samples generated by Igal using Pawel event generator
- Radiative corrections included
- Igal has implemented the generator to the GlueX framework (to be checked) !

## Slide 5
Compton Reconstruction
EFCAL + ECCAL - EBEAM (GeV)
TAGM counter 33
(E 9 GeV)
Run 61914
Subtract accidentals
Subtract background using empty target runs
Fit for event yield using a Crystal Ball function
EFCAL + ECCAL - EBEAM (GeV)
Accidentals

## Slide 6
Run 61914
Flux Normalized Yield

## Slide 7
Compton Cross Section
Note: there are uncertainties
in He target density
Shape of the cross section is
in a relatively good agreement
with theoretical predictions
need to check with larger statistics