## Slide 1: Central Drift Chamber Update
GlueX Collaboration Meeting, Indiana University, May 2011
Naomi Jarvis
Carnegie Mellon University

## Slide 2: The CDC Team
CDC Update
Project Leader: Curtis Meyer
Project Scientist: Naomi Jarvis
Construction Manager: Gary Wilkin
Technicians: Amy Woodhall, Kaitlin Mueller
Undergraduate Students:
2011: Rahul Kurl, Maddi Brumbaugh
+ …

## Slide 3: Outline
CDC Update
CDC Construction
Current status
Prep work for next stage
Prototype studies

## Slide 4: CDC Construction: Current status
CDC Update
Phase 1: Mounting and Alignment of Endplates
complete
Phase 2: Installation of Straws (gas lines + outer shell)
Completed rows 1-19 of 28
Used up straws – rest expected soon
Phase 3: Wire Stringing
Started work on row 1

## Slide 5: CDC Construction: Phase 2 Components
CDC Update
Component | Status | Acceptance
Straws (1900) | Checked, trimmed, installed | 82%
Straws (250) | Checked, trimmed, installed | 90%
Straws (rest) | Pending | 
Al donuts | Checked, cleaned, some installed | ~ 100%
Al feedthrus | Checked, cleaned, some installed | ~ 100%
Noryl donuts | Checked, cleaned, some installed | ~ 100%
Noryl feedthrus | Checked, cleaned, some installed | ~ 100%
Gas lines + steel nipples |  | 
Gas line glue widgets | To be made at CMU | 
Outer shell | Arrived at CMU 3rd May | 
Outer hub material |  | 
Tape for outer shell | Duct tape is at CMU; need Cu tape | 

## Slide 6
CDC Update

## Slide 7: CDC Construction: Phase 3 Components
CDC Update
Component | Status | Acceptance
Pinholders | 85% checked, cleaned, some installed | So far all but 1
Crimp pins | Some in clean storage, some installed | 100%
Wire | Some in clean storage, some installed | 100%

## Slide 8
CDC Update

## Slide 9: CDC Construction: Phase 4 Components
CDC Update
Component | Status | Acceptance
Threaded bushings | At CMU | 
O-rings | At CMU | 
Lugged ferrules | CMU have ordered these | 
Wire | At CMU | 100%
Silver balls | At CMU | 100%
Heatshrink | At CMU | 100%
Standoffs (3 types) |  | 
Standoff screws |  | 
HVBs |  | 

## Slide 10: CDC Construction: Phase 4 Preparations
CDC Update
Hook-up wires
20% are half-made
HVB connection layout
Aim for shortest max wire lengths

## Slide 11: Prototype studies
CDC Update
New fADC125, preamp, plenum, gas MFCs
CODA 2.5, cosmic ray data, 50/50 Ar/CO2

## Slide 12: Event fADC data
CDC Update
Cosmic ray data with small prototype – event in one straw shown
Using 512 x 8ns samples and fADC range 0-4095
Noise is ~ 11 ADC values

## Slide 13: Amplitude histogram
CDC Update
Calculate mean pedestal for first 100 samples in each 100 events
Subtract pedestal from ADC values
Select event where ADC value rises above a threshold (5 sigma): hit
Histogram the first maximum in the ADC value after crossing the threshold

## Slide 14: Integrated amplitude histogram
CDC Update
Subtract mean pedestal from ADC values
Select event where ADC value rises above a threshold (5 sigma): hits
Sum the ADC values from the threshold crossing point out to 664ns later

## Slide 15: Drift-time histogram
CDC Update
Define leading edge in ADC data (bins with step > 0.3 x max step)
Extract time by DCOG (average of leading edge bins weighted by step size)
Select events with 5 or more hits
Histogram drift times and extract t-zero from histogram: fit leading edge/take point on edge

## Slide 16: Tracking
CDC Update
Select events with 5+ hits
Use Garfield simulation to convert drift time into distance by interpolation
Find track – look at each pair of hits, calculate 2 possible straight line tracks, include other hits, find the most likely track
Fit track – send the most likely track to minuit to fit radius
Calculate residuals – distance between fitted track radius and interpolated driftdistance, and again after excluding the straw of interest from the fit
Adjust tzero? times < tzero are assigned to tzero

## Slide 17: Resolution
CDC Update
Prototype horizontal, tzero = maximum bin in drift time histogram

## Slide 18: Resolution
CDC Update
Prototype 45°, tzero = maximum bin in drift time histogram

## Slide 19: Resolution
CDC Update
Prototype 45°, tzero = half-way up leading edge of drift time histogram
Leading edge: counts>10% of max counts, fit to straight line, find start

## Slide 20: What next?
CDC Update
Prototype
Tune the timing methods
Put algorithm onto fADC
Revisit integration method
Revisit gas mix and flow rates
CDC Phase 2
Straw installation
Also need to install gas lines and shell.
Wire tension tests
Phase 3 Stringing (2011/2012)
Phase 4 Electrical hookup
Some details to be finalized
Remaining:
Operational testing, transport