Gluex Detector Tasks/Status

Solenoid

- Coil repairs contract in process

- Upstream ring in process of getting machined

- Designer needed ½ time to work on cryogenics and structure

- Support structure– need to tie in with BCAL

- Need to tie in with Target cryogenic system

- ½ time designer to be available in January

UPV

- On hold

Target

- Action tracker updated to reflect geometry questions for target

- Met with Mike Seely and determined input for tracker

- Maybe get Werner to do some research on target dimensions?

- Need to talk with Steve Christo about reducing 4cm diam.

Start Counter

- Werner to put out geometry specification soon. He is looking at the shape of the scintillators also

- 40 channels

CDC

- Bill to look at FDC/CDC rails

- Need to take a closer look at feedthru and gas plenum. Tim at CMU this week

- Need to Design insertion tooling

- Develop alignment scheme and features (all permanent features must be non-magnetic)

- Slava to begin looking at design

- Need to talk to Brian and Simon about mixing methane into gas system

BCAL

- Review and update current insertion concept)

- Regina looking at machinability of wedges

- Make scale model

- Design assy/installation cart (in process)

- Where is layup and machining going to take place? All in Alberta?

FDC

- Latest cooling scheme (24 circuits total with florinert) looks to be acceptable

- Include cooling scheme on prototype

- Produce prototype baseline drawings – first cut almost done- if all is well, these will be the production dwgs also

- Deflection test on wireframe successful

- Bill to look at FDC/CDC rails

- Look at strong back design

- Design installation tooling

- Bill investigating o-ring materials and compression

Cerenkov

- On hold

TOF

- Develop concept for connecting to FCAL (in process)

- Develop (with Matt Sheppard) support structure concept (in process)

FCAL

- Need to revisit lead glass frame

- Beni working on temperature, cookie pressure and machining test piece

- Design support structure with rails (preliminary).

- Add dark room with cooling (preliminary)

- Paul to rerun magnetic shielding analysis

- Look into doing a mag field test on 8x8 array

Tagger

- Need to double check the Protvino vs. Autocad model

- SOW and Spec written

- Interface dwg in work (discrepancy with civil)

Hodoscope

- Have initial assy dwg from Richard and Franz

Microoscope

- Have initial assy dwg

Collimator

- Have initial assy dwg and some details

Pair Spectrometer

- Have initial assy dwg from Hall B

- Trying to contract Yerevan to write spec.

Radiator

- Look at Goniometer from German company

- New support for thin radiator to be designed

Infrastructure

- Develop Platforms designs  (Front, Rear, Side)

- Develop cable routing scheme, work with elecrical

- Perform global cooling analysis

- Need to Update rack quantities and positions